## Slide 1: Capacitor degradation model
Aqarib Hussain

## Slide 2: Testbed and Flight profile
eVTOL flight profile and Load profile.
Testbed setup.

## Slide 3: How can Capacitor degradation affect evtol powertrain ?
[1] H. Wang, M. Liserre and F. Blaabjerg, "Toward Reliable Power Electronics: Challenges, Design Tools, and Opportunities," in IEEE Industrial Electronics Magazine, vol. 7, no. 2, pp. 17-26, June 2013, doi: 10.1109/MIE.2013.2252958.v
Failure distribution among major components [1].
Few causes of capacitor failure include exceeding the maximum ratings for the following parameters:
  The ripple current
  Ambient temperature
  Operating Voltage

## Slide 4: Degradation model studied
Model 1:
Where
L : Expected life in actual use [hour]
T: Actual ambient temperature + temperature rise due to ripple current [∘ C]
Lo : Guaranteed life of capacitor [hour]
To : 1) Product that defines the endurance by superimposing the rated ripple current. Upper category temperature of capacitor + temperature rise (5∘C) due to rated ripple current [∘C]
2) Product that defines the endurance by applying a rated voltage. Upper category temperature of capacitor [∘ C]
L1 : Guaranteed life (h) at temperature T1 (℃).
L2 : Expected life (h) at temperature T2 (℃) * In the case of a hybrid type, category temperature (℃).
T1 : Upper category temperature (℃) + temperature increase caused by rated ripple current (℃).
T2 : Ambient temperature of capacitor (℃).
⊿T : Temperature increase caused by ripple current (℃) .
https://industrial.panasonic.com/content/data/CP/PDF/Alumi/Alumi_TechnicalGuide_e.pdf
https://industrial.panasonic.com/cdbs/www-data/pdf/RDF0000/ABA0000C1026.pdf

## Slide 5
Model 2:
= expected operating lifetime
= Actual lifetime
= Actual applied voltage
= Rated output voltage
n= constant (3-5)
= rated temperature
= maximum ambient temperatures
Reliability of Capacitors for DC-Link Applications in Power Electronic Converters—An Overview Huai Wang, Member, IEEE, and Frede Blaabjerg, Fellow, IEEE

## Slide 6: A comparison of models
Model 1
Do not consider voltage
Takes less information from physical system
Rarely used
Model 2
Includes voltage
Takes more information form physical system
Commonly used

## Slide 7: Proposed capacitor degradation model -DT
Block diagram showing DATA exchange between PT and DT.

## Slide 8: DT Results
LabVIEW setup.
Plots for Real time data from testbed data for 300 sec.
Analytical model in Matlab.
Plots for Real time data from testbed data for 60 sec.

## Slide 10: Thanks!
Name : Aqarib Hussain
Email : ahussain@email.sc.edu